## Slide 1: I/O Systems Lesson 1 Introduction
David Liu
Fall 2021

## Slide 2: Learning Outcomes
Explore the structure of an operating system’s I/O subsystem
Discuss the principles and complexities of I/O hardware
Explain the performance aspects of I/O hardware and software

## Slide 3: I/O Hardware
Incredible variety of I/O devices
  Storage
  Transmission
  Human-interface

## Slide 4: I/O Hardware Common concepts
Signals from I/O devices interface with computer
  Port – connection point for device
  Bus - daisy chain or shared direct access
    PCI bus common in PCs and servers, PCI Express (PCIe)
    expansion bus connects relatively slow devices
    Serial-attached SCSI (SAS) common disk interface
  Controller (host adapter) – electronics that operate port, bus, device
    Sometimes integrated
    Sometimes separate circuit board (host adapter)
    Contains processor, microcode, private memory, bus controller, etc
      Some talk to per-device controller with bus controller, microcode, memory, etc

## Slide 5: A Typical PC Bus Structure

## Slide 6: I/O Hardware (Cont.)
Fibre channel (FC) is complex controller, usually separate circuit board (host-bus adapter (HBA)) plugging into bus
I/O instructions control devices
Devices usually have registers where device driver places commands, addresses, and data to write, or read data from registers after command execution
  Data-in register, data-out register, status register, control register
  Typically 1-4 bytes, or FIFO buffer
Devices have addresses

## Slide 7: Device I/O Port Locations on PCs (partial)

## Slide 8: I/O Hardware Device Control
Special I/O instructions
Memory-mapped I/O
  Device data and command registers mapped to processor address space
  Especially for large address spaces (graphics)
Now commonly memory-mapped I/O

## Slide 9: Polling
For each byte of I/O
  (host) Read busy bit from status register until busy bit is 0
  Host sets read or write bit and if write copies data into data-out register
  Host sets command-ready bit
  Controller sets busy bit, executes transfer
  Controller clears busy bit, error bit, command-ready bit when transfer done
Step 1 is busy-wait cycle to wait for I/O from device
  Reasonable if device is fast
  But inefficient if device slow
  CPU switches to other tasks?
    But if miss a cycle data overwritten / lost
    e.g. small buffer when streaming data)

## Slide 10: Interrupts
Polling can happen in 3 instruction cycles
  Read status, logical-and to extract status bit, branch if not zero
  How to be more efficient if non-zero infrequently?
CPU Interrupt-request line triggered by I/O device
  Checked by processor after each instruction
Interrupt handler receives interrupts
  Maskable to ignore or delay some interrupts
Interrupt vector to dispatch interrupt to correct handler
  Context switch at start and end
  Based on priority
  Some nonmaskable
  Interrupt chaining if more than one device at same interrupt number

## Slide 11: Interrupt-Driven I/O Cycle

## Slide 12: Intel Pentium Processor Event-Vector Table

## Slide 13: Interrupt Numbers
Stressing interrupt management because even single-user systems
  manage hundreds or interrupts per sec
  servers hundreds of thousands per sec
For example, a quiet macOS desktop generated 23,000 interrupts over 10 seconds

## Slide 14: Interrupts Mechanism for Other Usage
Interrupt mechanism also used for exceptions
  Terminate process, crash system due to hardware error
Page fault executes when memory access error
System call executes via trap to trigger kernel to execute request
Multi-CPU systems can process interrupts concurrently
  If operating system designed to handle it
Used for time-sensitive processing, frequent, must be fast

## Slide 15: Direct Memory Access
Used to avoid programmed I/O (one byte at a time) for large data movement
Offload from CPU to DMA controller
Bypasses CPU to transfer data directly between I/O device and memory
OS writes DMA command block into memory
  Source and destination addresses
  Read or write mode
  Count of bytes
  Writes location of command block to DMA controller
  Bus mastering of DMA controller – grabs bus from CPU
    Cycle stealing from CPU but still much more efficient
  When done, interrupts to signal completion
Version that is aware of virtual addresses can be even more efficient - DVMA

## Slide 16: Six Step Process to Perform DMA Transfer