## Slide 1: I/O Systems Lesson 3 Kernel I/O Systems
David Liu
Fall 2021

## Slide 2: Kernel I/O Subsystem
Scheduling
  Some I/O request ordering via per-device queue
  Some OSs try fairness
  Some implement Quality Of Service (i.e. IPQOS)
Buffering - store data in memory while transferring between devices
  To cope with device speed mismatch
  To cope with device transfer size mismatch
  To maintain “copy semantics”
  Double buffering – two copies of the data
    Kernel and user
    Varying sizes
    Full / being processed and not-full / being used
    Copy-on-write can be used for efficiency in some cases

## Slide 3: Device-status Table

## Slide 4: Common PC and Data-center I/O devices and Interface Speeds

## Slide 5: Kernel I/O Subsystem
Caching - faster device holding copy of data
  Always just a copy
  Key to performance
  Sometimes combined with buffering
Spooling - hold output for a device
  If device can serve only one request at a time
  i.e., Printing
Device reservation - provides exclusive access to a device
  System calls for allocation and de-allocation
  Watch out for deadlock

## Slide 6: Error Handling
OS can recover from disk read, device unavailable, transient write failures
  Retry a read or write, for example
  Some systems more advanced – Solaris FMA, AIX
    Track error frequencies, stop using device with increasing frequency of retry-able errors
Most return an error number or code when I/O request fails
System error logs hold problem reports

## Slide 7: I/O Protection
User process may accidentally or purposefully attempt to disrupt normal operation via illegal I/O instructions
  All I/O instructions defined to be privileged
  I/O must be performed via system calls
    Memory-mapped and I/O port memory locations must be protected too

## Slide 8: Use of a System Call to Perform I/O

## Slide 9: Kernel Data Structures
Kernel keeps state info for I/O components, including open file tables, network connections, character device state
Many, many complex data structures to track buffers, memory allocation, “dirty” blocks
Some use object-oriented methods and message passing to implement I/O
  Windows uses message passing
    Message with I/O information passed from user mode into kernel
    Message modified as it flows through to device driver and back to process
    Pros / cons?

## Slide 10: UNIX I/O Kernel Structure

## Slide 11: Power Management
Not strictly domain of I/O, but much is I/O related
Computers and devices use electricity, generate heat, frequently require cooling
OSes can help manage and improve use
  Cloud computing environments move virtual machines between servers
    Can end up evacuating whole systems and shutting them down
Mobile computing has power management as first class OS aspect

## Slide 12: Power Management (Cont.)
For example, Android implements
  Component-level power management
    Understands relationship between components
    Build device tree representing physical device topology
    System bus -> I/O subsystem -> {flash, USB storage}
    Device driver tracks state of device, whether in use
    Unused component – turn it off
    All devices in tree branch unused – turn off branch
  Wake locks – like other locks but prevent sleep of device when lock is held
  Power collapse – put a device into very deep sleep
    Marginal power use
    Only awake enough to respond to external stimuli (button press, incoming call)

## Slide 13: Power Management (Cont.)
Modern systems use advanced configuration and power interface (ACPI) firmware providing code that runs as routines called by kernel for device discovery, management, error and power management

## Slide 14: Kernel I/O Subsystem Summary
In summary, the I/O subsystem coordinates an extensive collection of services that are available to applications and to other parts of the kernel
  Management of the name space for files and devices
  Access control to files and devices
  Operation control (for example, a modem cannot seek())
  File-system space allocation
  Device allocation
  Buffering, caching, and spooling
  I/O scheduling
  Device-status monitoring, error handling, and failure recovery
  Device-driver configuration and initialization
  Power management of I/O devices
The upper levels of the I/O subsystem access devices via the uniform interface provided by the device drivers