## Slide 1: Main Memory Lesson 2 Memory Allocation and Paging
David Liu
Fall 2021

## Slide 2: Process Memory Allocation
Contiguous Memory Allocation
Paging
  Fixed-sized blocks: frames in physical memory or pages in logical memory

## Slide 3: Contiguous Allocation
Main memory must support both OS and user processes
Limited resource, must allocate efficiently
Contiguous allocation is one early method
Main memory usually into two partitions:
  Resident operating system, usually held in high memory with interrupt vector
  User processes then held in low memory
  Each process contained in single contiguous section of memory

## Slide 4: Hardware Support for Relocation and Limit Registers

## Slide 5: Variable Partition
Multiple-partition allocation
  Degree of multiprogramming limited by number of partitions
  Variable-partition sizes for efficiency (sized to a given process’ needs)
  Hole – block of available memory; holes of various size are scattered throughout memory
  When a process arrives, it is allocated memory from a hole large enough to accommodate it
  Process exiting frees its partition, adjacent free partitions combined
  Operating system maintains information about: a) allocated partitions b) free partitions (hole)

## Slide 6: Dynamic Storage-Allocation Problem
First-fit: Allocate the first hole that is big enough
Best-fit: Allocate the smallest hole that is big enough; must search entire list, unless ordered by size
  Produces the smallest leftover hole
Worst-fit: Allocate the largest hole; must also search entire list
  Produces the largest leftover hole
How to satisfy a request of size n from a list of free holes?
First-fit and best-fit better than worst-fit in terms of speed and storage utilization

## Slide 7: Fragmentation
External Fragmentation – total memory space exists to satisfy a request, but it is not contiguous, CAN NOT BE USED
Internal Fragmentation – allocated memory may be slightly larger than requested memory; this size difference is memory internal to a partition, but not being used
First fit analysis reveals that given N blocks allocated, 0.5 N blocks lost to fragmentation
  1/3 may be unusable -> 50-percent rule

## Slide 8: External Fragmentation Solutions
Compaction
  Shuffle memory contents to place all free memory together in one large block
  Compaction is possible only if relocation is dynamic, and is done at execution time
  Expensive
Allow non-contiguous memory allocation: Paging

## Slide 9: Paging I
Physical address space of a process can be noncontiguous; process is allocated physical memory whenever the latter is available
  Avoids external fragmentation
  Avoids problem of varying sized memory chunks
Divide physical memory into fixed-sized blocks called frames
  Size is power of 2, between 512 bytes and 16 Mbytes
Divide logical memory into blocks of same size called pages

## Slide 10: Paging II
Keep track of all free frames
To run a program of size N pages, need to find N free frames and load program
Set up a page table to translate logical to physical addresses
Still have Internal fragmentation (average size of a page)

## Slide 11: Address Translation Scheme
Logical Address generated by CPU is divided into:
  Page number (p) – used as an index into a page table which contains base address of each page in physical memory
  Page offset (d) – combined with base address to define the physical memory address that is sent to the memory unit
  For given logical address space 2m and page size 2n
  Page size is determined by hardware

## Slide 12: Paging Hardware

## Slide 13: Paging Model of Logical and Physical Memory

## Slide 14: Paging Example
Logical address:
  n = 2 and m = 4.
  page size of 4 bytes
  a physical memory of 32 bytes (8 pages)
Page 0
Frame 5

## Slide 15: Paging -- Calculating internal fragmentation
Page size = 2,048 bytes (2 KB, n=11)
Process size = 72,766 bytes
35 pages + 1,086 bytes
Internal fragmentation of 2,048 - 1,086 = 962 bytes
Worst case fragmentation = 1 frame – 1 byte
On average fragmentation = 1 / 2 frame size
So small frame sizes desirable? -> larger page table
But each page table entry takes memory to track
Page sizes growing over time
  Solaris supports two page sizes – 8 KB and 4 MB

## Slide 16: Free Frames
Before allocation
After allocation

## Slide 17: Implementation of Page Table
Page table is kept in main memory
  Page-table base register (PTBR) points to the page table
  Page-table length register (PTLR) indicates size of the page table
In this scheme every data/instruction access requires two memory accesses
  One for the page table
  one for the data / instruction
The two memory access problem can be solved by the use of a special fast-lookup hardware cache called translation look-aside buffers (TLBs) (also called associative memory).

## Slide 18: Translation Look-Aside Buffer
Some TLBs store address-space identifiers (ASIDs) in each TLB entry – uniquely identifies each process to provide address-space protection for that process
  Otherwise need to flush at every context switch
TLBs typically small (64 to 1,024 entries)
On a TLB miss, value is loaded into the TLB for faster access next time
  Replacement policies must be considered
  Some entries can be wired down for permanent fast access

## Slide 19: Associative Memory
Associative memory (CAM, Content-addressable Memory)
  parallel search
  Compared with all keys simultaneously
Address translation (p, d)
  If p is in associative register, get frame # out
  Otherwise get frame # from page table in memory

## Slide 20: TLB Lookup in Pipelining
TLB lookup is part of instruction pipeline
Adding no performance penalty

## Slide 21: Paging Hardware With TLB

## Slide 22: Effective Access Time
  Hit ratio – percentage of times that a page number is found in the TLB
An 80% hit ratio means that we find the desired page number in the TLB 80% of the time.
Suppose that 10 nanoseconds to access memory.
  If we find the desired page in TLB then a mapped-memory access take 10 ns
  Otherwise we need two memory access so it is 20 ns
Effective Access Time (EAT)
EAT = 0.80 x 10 + 0.20 x 20 = 12 nanoseconds
implying 20% slowdown in access time
Consider amore realistic hit ratio of 99%,
  EAT = 0.99 x 10 + 0.01 x 20 = 10.1ns
implying only 1% slowdown in access time.

## Slide 23: Memory Protection
Memory protection implemented by associating protection bit with each frame to indicate if read-only or read-write access is allowed
  Can also add more bits to indicate page execute-only, and so on
Valid-invalid bit attached to each entry in the page table:
  “valid” indicates that the associated page is in the process’ logical address space, and is thus a legal page
  “invalid” indicates that the page is not in the process’ logical address space
  Or use page-table length register (PTLR)
Any violations result in a trap to the kernel

## Slide 24: Valid (v) or Invalid (i) Bit In A Page Table

## Slide 25: Shared Pages
Shared code
  One copy of read-only (reentrant) code shared among processes (i.e., text editors, compilers, window systems)
  Similar to multiple threads sharing the same process space
  Also useful for interprocess communication if sharing of read-write pages is allowed
Private code and data
  Each process keeps a separate copy of the code and data
  The pages for the private code and data can appear anywhere in the logical address space

## Slide 26: Shared Pages Example