## Slide 1: Main Memory Lesson 5 Memory Architectures
David Liu
Fall 2021, Spring 2022

## Slide 2: Architecture Examples
Intel IA-32
x86-64 (started by AMD)
ARM ARMv8

## Slide 3: Intel IA-32 Architecture
Supports both segmentation and segmentation with paging
  Each segment can be 4 GB
  Up to 16 K segments per process
  Divided into two partitions
    First partition of up to 8 K segments are private to process (kept in local descriptor table (LDT))
    Second partition of up to 8K segments shared among all processes (kept in global descriptor table (GDT))

## Slide 4: Intel IA-32 Architecture
CPU generates logical address
  Selector: 16 bits
  Offset: 32 bits
IA-32 Linear Address
  segment base + offset
LDT or GDT
protection

## Slide 5: IA-32 Logical to Physical Address Translation

## Slide 6: Intel IA-32 Paging Architecture
Page_Size = 1
20 bits
20 bits
10
22
4MB page

## Slide 7: Intel IA-32 Page Address Extensions
page address extension (PAE), allowing 32-bit apps access to more than 4GB of memory space
  More than 4 GB space
  Paging went to a 3-level scheme
  Top two bits refer to a page directory pointer table
  Page-directory and page-table entries moved to 64-bits in size
  IA-32 address space
    20 + 12 = 32 232 = 4GB
    20 + 4 + 12 = 36 (PAE) 236 = 64GB
24 bits
24 bits

## Slide 8: x86-64
Current generation Intel x86 architecture
64 bits is ginormous (> 16 exabytes)
In practice only implement 48 bit addressing
  256 TB
  Page sizes of 4 KB, 2 MB, 1 GB
  Four levels of paging hierarchy
Can also use PAE so virtual addresses are 48 bits and physical addresses are 52 bits

## Slide 9: ARM Architecture
Dominant mobile platform chip (Apple iOS and Google Android devices for example)
Modern, energy efficient, 32-bit CPU
4 KB and 16 KB pages
1 MB and 16 MB pages (termed sections)
One-level paging for sections, two-level for smaller pages
Two levels of TLBs
  Outer level has two micro TLBs (one data, one instruction)
  Inner is single main TLB
  First inner is checked, on miss outers are checked, and on miss page table walk performed by CPU

## Slide 10: ARM Architecture
ARMv8
  64 bit
  48-bit used
or
or